## Slide 1
Raspberry Pi + ESP32 Robot
withLive Video Streaming&AI-based Control
ESP32
Live Streaming
AI Control
Robotics
2025-09-19

## Slide 2
System Overview
Three-component architecture with specialized roles and interconnected communication methods.
Windows PC
AI Decision-Making
Runs AI model
Processes video streams
Makes movement decisions
Raspberry Pi
Network & Command Relay
Streams video to PC
Relays commands to ESP32
Manages network communications
ESP32
Low-Level Hardware Control
Motor control
Sensor data acquisition
Real-time obstacle avoidance
MJPG Stream
HTTP Commands
UART Communication
* Using ESP32 instead of Arduino Nano for enhanced Wi-Fi and Bluetooth capabilities

## Slide 3
Hardware Components
Key hardware components for the Raspberry Pi + ESP32 robot system
Core Controllers
Raspberry Pi 4 (4GB RAM)
High-level processing for video streaming and network
ESP32
Real-time, low-level control with Wi-Fi/BT capabilities
Sensors
USB Webcam
Captures live video for streaming
Ultrasonic Sensor (HC-SR04)
Measures distances for obstacle avoidance
Motors & Power
Motor Driver (L298N/TB6612)
Interfaces between ESP32 and DC motors
Voltage Divider for UART
Ensures safe communication between ESP32 and Pi
Raspberry Pi 4
HC-SR04 Ultrasonic
L298N Motor Driver
DC Motors & Wheels

## Slide 4
Circuit Connections
Establishing reliable communication between Raspberry Pi and ESP32 is crucial for robot operation.
UART Communication
Connection Scheme:
ESP32 TX → Raspberry Pi RX
ESP32 RX → Raspberry Pi TX
Communication Flow:
Commands from PC → ESP32 via UART
Sensor data from ESP32 → Raspberry Pi
Example: Raspberry Pi with multiple Arduino boards via UART
Voltage Compatibility
Raspberry Pi: 3.3V logic levels
ESP32: 3.3V or 5V operation
Voltage Mismatch:Use voltage divider or logic level shifter
Common Ground Connections
Essential for:
Proper signal integrity
Preventing erratic behavior
Connecting GND pins of all modules

## Slide 5
Software Setup (Pi)
Configuring the Raspberry Pi as the central hub for video streaming and command relay
MJPG-Streamer
Captures video from USB webcam and streams over network
# Stream URL:
http://<Pi_IP>:8080/?action=stream

## Slide 6
Video Streaming
MJPG-Streamer implementation for Raspberry Pi to capture and stream video for AI processing.
Video Source
USB Webcam
Raspberry Pi
MJPG-Streamer
Network
Wi-Fi Streaming
Destination
PC/AI Processing
Configuration Settings
Resolution
640x480 pixels
Frame Rate
20fps
Stream URL
http://<Raspberry_Pi_IP>:8080/?action=stream
Access Methods
Web Browser
Direct access
VLC
Media player
OpenCV
AI processing
Mobile
Remote viewing

## Slide 7
Command Handling
Flask server on Raspberry Pi receives and processes control commands for the ESP32.
Windows PC
AI Decision-Making
Sends HTTP POST requests
HTTP
Raspberry Pi
Flask Server
Forwards via UART
UART
ESP32
Motor Control
Sends status back
Flask Server Implementation
/move endpoint:Receives POST requests with movement commands
Command mapping:Translates commands to simple codes (F/B/L/R/S)
PySerial:Forwards commands to ESP32 via UART
Security & Feedback
Token Authentication:Secure command execution
/status endpoint:Displays feedback from ESP32
Real-time feedback:System status and sensor data

## Slide 8
ESP32 Logic
ESP32 Role
The ESP32 functions as the real-time control unit, handling low-level hardware interactions and time-critical operations.
UART Command Listening
Continuously monitors UART interface
Receives single-character commands (F/B/L/R/S)
Interfaces with Raspberry Pi via TX/RX
Motor Control
Controls DC motors via L298N/TB6612 driver
Executes movement commands
Handles forward/backward directions
Ultrasonic Obstacle Avoidance
Monitors distance using HC-SR04 sensor
Overrides commands if obstacle detected
Prevents collisions at critical distances
Feedback to Raspberry Pi
Sends status information via UART
Provides obstacle distance data
Enables PC-side monitoring
Process Flow:ESP32 receives commands → executes motor actions → monitors obstacles → sends feedback

## Slide 9
Windows PC (AI Side)
The Windows PC hosts the AI model and serves as the decision-making center for the robot.
OpenCV
Captures MJPG video stream from Raspberry Pi
Real-time frame grabbing
Processing for AI analysis
AI Model
Analyzes video frames to make decisions
Object recognition
Movement planning
HTTP Requests
Sends commands to Raspberry Pi
HTTP POST requests
Command translation (F/B/L/R/S)
Example Implementation
OpenCV Video Capture
cap = cv2.VideoCapture('http://pi:8080/stream')

## Slide 10
Workflow
Closed-loop operation integrating video streaming, AI-driven decision-making, and real-time motor control.
Video Streaming
Raspberry Pi streams live video over Wi-Fi using MJPG-Streamer.
AI Decision-Making
Windows PC processes video frames and makes movement decisions.
Command Transmission
PC sends HTTP POST requests with movement commands to Raspberry Pi.
UART Forwarding
Raspberry Pi forwards commands via UART to ESP32.
Obstacle Avoidance
ESP32 monitors surroundings with ultrasonic sensor and autonomously avoids obstacles.
* System continuously loops, enabling dynamic and intelligent robot navigation

## Slide 11
Benefits & Extensions
Project Benefits
Clean Division of Labor
Raspberry Pi handles high-level tasks while ESP32 manages low-level, time-critical operations.
Scalability
Modular design allows easy expansion with additional sensors, cameras, or AI features.
Cost-Effectiveness
Affordable hardware provides accessible entry into robotics and AI for education and hobbyists.
Robustness
ESP32's independent obstacle avoidance provides safety even if AI or Raspberry Pi communication fails.
Future Extensions
H.264 Streaming
Transition from MJPG to H.264 for improved compression, reduced bandwidth, and higher quality video.
ROS Integration
Integrate Robot Operating System for sophisticated navigation, task planning, and sensor fusion.
Cloud AI
Deploy AI model to cloud for greater computational resources, enabling more advanced algorithms.
Additional Sensors
Add LiDAR, depth cameras, or IMUs for richer environmental understanding and enhanced autonomy.

## Slide 12
Conclusion
Project Achievements
This project successfully demonstrates anaffordable and integrated robotics platform, effectively combining:
Live video streaming with MJPG-Streamer
AI-based decision-making from Windows PC
Real-time motor control with ESP32
Autonomous obstacle avoidance capabilities
Core Principles Demonstrated
IoT
Connected device ecosystem with Raspberry Pi as an edge gateway
Edge Computing
Data processing at the network edge with Raspberry Pi and ESP32
Robotics Control
Hierarchical control system with PC, Raspberry Pi, and ESP32
Integration
Modular architecture for easy expansion and future development
Next Steps
This project provides a robust foundation for further experimentation:
Enhance with H.264 streaming
Integrate with ROS for navigation
Deploy AI to cloud platforms